## Slide 1
CARD
VALID
SMART INDIA HACKATHON 2026
Praman Setu
Digital companion for field drug testing
A camera-led, offline-first workflow for calibrated presumptive results and tamper-evident field records.
SIH26231
MHA / SOFTWARE
SIMULATED PROTOTYPE - NOT A DRUG TEST
01

## Slide 2
01 / THE GAP
The field result is visible. The evidence is not.
02
Today, a color change is interpreted by eye -
with no consistent calibration and no verifiable record of the moment it happened.
01
SUBJECTIVE
Different officers can read the same color differently.
02
UNVERIFIED
No camera evidence, calibrated reference, or chain of custody.
03
DISCONNECTED
Kit batch, timing, place, and operator data are easy to lose.
04
OFFLINE
Field connectivity cannot be assumed at the point of testing.
The opportunity
Turn one subjective color reading into a documented, repeatable field workflow.
PRAMAN SETU / SIH26231
SIMULATED PROTOTYPE - PRESUMPTIVE RESULT ONLY

## Slide 3
02 / THE SOLUTION
Praman Setu makes the test traceable.
03
One flow. Three layers of confidence.
01
CALIBRATE
Use six reference patches and white-patch gain correction to normalize the captured image.
02
CLASSIFY
Measure the reaction region in LAB space, compare with Delta E, and surface confidence plus uncertainty.
03
PROVE
Bind the image, metadata, timing, GPS, operator, hash, signature, and chain position into one record.
Works with existing kits. No new hardware. Offline first.
Output: a presumptive field-test result and supporting digital record - never a replacement for laboratory confirmation.
PRAMAN SETU / SIH26231
SIMULATED PROTOTYPE - PRESUMPTIVE RESULT ONLY

## Slide 4
03 / THE WORKFLOW
From camera frame to verifiable record
04
CAPTURE
Reference card + kit
1
CALIBRATE
Six patches + gain
2
MEASURE
ROI + LAB + Delta E
3
RECORD
Hash + chain + sign
4
VERIFY
JSON + image + QR
5
Every transition is explicit
KIT VALIDATED -> TIMER RUNNING -> CAPTURE WINDOW -> CARD VALID -> RESULT READY -> SAVED -> EXPORTED
Hard gates stop the workflow; soft quality signals explain uncertainty.
PRAMAN SETU / SIH26231
SIMULATED PROTOTYPE - PRESUMPTIVE RESULT ONLY

## Slide 5
04 / CLASSIFICATION
The app does not guess. It measures, gates, and explains.
05
REFERENCE CARD
Tap six known patches
White / black / red / green / blue / gray
CARD VALID
1
Calibrate
White-patch gain correction
Reference-card validation
Card version + residual Delta E
2
Measure
Sample ROI median RGB -> LAB
Delta E against the Reference DB
Confidence + uncertainty
3
Gate
Blur / clipping / glare / ROI spread
Timing window / card validity
Preliminary result or Inconclusive
PRAMAN SETU / SIH26231
SIMULATED PROTOTYPE - PRESUMPTIVE RESULT ONLY

## Slide 6
05 / INTEGRITY
Evidence is designed as a bundle, not a screenshot.
06
The original image stays untouched. The analysis copy can change; the evidence identity cannot.
ORIGINAL IMAGE
SHA-256
CANONICAL JSON
record bytes
HASH CHAIN
previous_hash
SIGNATURE
device key + public key
EXPORT
JSON + image + PDF + QR
VERIFY.HTML
recomputes the image hash | checks the signature | walks the chain | reports each status separately
Prototype limitation: this is tamper-evident evidence, not trusted timestamping or agency PKI.
PRAMAN SETU / SIH26231
SIMULATED PROTOTYPE - PRESUMPTIVE RESULT ONLY

## Slide 7
06 / OPERATIONS
Built for the field: offline first, reviewable later.
07
01
OFFLINE QUEUE
Every test is saved locally before synchronization.
PENDING -> SYNCED
PENDING -> FAILED
FAILED -> RETRY
Local evidence is retained in every state.
02
SUPERVISOR REVIEW
Read-only review of result, capture quality, kit, timing, metadata, and sync state.
REVIEWED
REQUIRES RETEST
REQUIRES LAB CONFIRMATION
03
RETEST, NOT MERGE
Test 2 links to Test 1 through retest_of.
Each record keeps its own image, hash, signature, and chain position.
Comparison is display-only.
Field reality is a first-class requirement, not an edge case.
PRAMAN SETU / SIH26231
SIMULATED PROTOTYPE - PRESUMPTIVE RESULT ONLY

## Slide 8
07 / ARCHITECTURE
A thin mobile workflow around a strong evidence core.
08
EXPERIENCE
React Native screens, navigation, role routes
WORKFLOW
test state machine, timer, quality gates
DOMAIN
calibration, LAB/Delta E, evidence builder
ADAPTERS
VisionCamera, OpenCV, SQLite, GPS, keys, PDF
VERIFY
canonical JSON + image + signature checks
PROTOTYPE
BOUNDARY
Bundled Reference DB
Local SQLite
Mock sync adapter
Prototype signing
No legal-evidence claim
One canonical export contract connects the app to verify.html.
PRAMAN SETU / SIH26231
SIMULATED PROTOTYPE - PRESUMPTIVE RESULT ONLY

## Slide 9
08 / DEMONSTRATION
The demo proves the workflow without pretending to prove a drug.
09
SIMULATED
- NOT A DRUG TEST
Use printed swatches, colored-water vials, simulated pouches, or printed rectangles. Never attach a simulated color to a named substance.
The judge sees the same controls: QR validation, timer lock, card validation, quality gate, retest, verification, and review.
JUDGE FLOW
01
Scan
Valid kit QR continues; expired kit blocks.
02
Capture
Reference card + simulated sample.
03
Classify
Preliminary result with confidence.
04
Prove
Hash, signature, PDF, QR, verification.
Every screen carries the presumptive-result disclaimer.
PRAMAN SETU / SIH26231
SIMULATED PROTOTYPE - PRESUMPTIVE RESULT ONLY

## Slide 10
09 / IMPACT
A stronger field record, without changing the field kit.
010
Praman Setu does not replace the chemistry. It improves the moment around it.
CONSISTENCY
Calibrated image capture reduces subjective color interpretation.
ACCOUNTABILITY
Timestamp, GPS, operator, kit, timing, and image identity travel together.
CONTINUITY
Offline records survive weak connectivity and can be reviewed later.
CAUTION
Inconclusive results and laboratory confirmation remain visible, never hidden.
Prototype deliverable: a working, explainable, judge-ready field workflow.
PRAMAN SETU / SIH26231
SIMULATED PROTOTYPE - PRESUMPTIVE RESULT ONLY

## Slide 11
Praman Setu
Make the presumptive result visible.
Make the record verifiable.
SIH26231 / Ministry of Home Affairs / Software
CAPTURE
+
CALIBRATE
+
VERIFY
SIMULATED PROTOTYPE - PRESUMPTIVE RESULT ONLY
11